## Slide 1: PERSONALIZED EXOSKELETON CONTROL FOR OPTIMIZING GAIT ECONOMY IN STROKE SURVIVORS
Daniel Rodriguez-Jorge, Gregory Sawicki, Aaron Young
August 14th, 2025
American Society of Biomechanics (Pittsburgh, PA)
Advances in Biomechanics with the power of AI & ML
Notes: Notes:

## Slide 2: Summary
Introduction
Generalizable exoskeleton control post-stroke using neural networks
Personalized, human-in-the-loop optimization
Preliminary experimental results
Conclusion
Introduction
Generalizable controller
Optimization
Conclusion

## Slide 3: Introduction
Millions with reduced independence, increased metabolic cost, and risk of health complications [1]
Exoskeletons to restore mobility face critical barriers. Limited adaptability to individual gait patterns post-stroke
We want to personalize exoskeleton assistance beyond biotorque for reduced energy cost post-stroke with no metabolic masks
Introduction
Generalizable controller
Optimization
Conclusion
[1] Murray et al. (2007), Reviews in Clinical Gerontology 17(4)

## Slide 4: Generalizable exoskeleton control post-stroke using neural networks
Introduction
Generalizable controller
Optimization
Conclusion
Large amounts of data are required for joint torques in clinical populations
Collected stroke data in different tasks, N = 20
Data to train AI models that are generalizable across subjects and tasks
θ, dθ, motion
ors

## Slide 5: Generalizable exoskeleton control post-stroke using neural networks
Collected data was used to train a Temporal Convolutional Neural Network to estimate total hip moments in real-time using the sensor suit
Introduction
Generalizable controller
Optimization
Conclusion
θ, dθ, motion
ors
[2] Molinaro et al. (2024), Science Robotics 9
Notes: A neural network is a computational model made of layers of interconnected “neurons” that learn to detect patterns in data. Each neuron applies a simple mathematical transformation, and by stacking many layers, the network can represent complex relationships—enabling tasks like prediction, classification, and generation.
A Temporal Convolutional Network (TCN) is a convolutional neural network architecture for sequence modeling that replaces recurrence with causal, dilated 1-D convolutions. It ensures predictions at time t depend only on the present and past (causality), and uses dilation to capture long-range dependencies efficiently.

## Slide 6: Generalizable exoskeleton control post-stroke using neural networks
Modular robotic hip exoskeleton for stroke patients, device-agnostic sensor layout
Using neural networks to estimate joint torque as in [2]
Reduced metabolic cost vs no exoskeleton with device-specific training data [3]
Introduction
Generalizable controller
Optimization
Conclusion
Mjoint*
θ, dθ, motion
ors
Texo
[2] Molinaro et al. (2024), Science Robotics 9
[3] Molinaro et al. (2024), Nature 635
Notes: How we remove masks with cool Ryan paper, and nature paper. Cite Greg relationship between mech work and metabolic work.

## Slide 7: Personalized, human-in-the-loop optimization
Mjoint*
θ, dθ, motion
Pjoint*(+)
ors
Texo
Pexo(+)
+
-
Ang veljoint*
Pbio(+)
Introduction
Generalizable controller
Optimization
Conclusion
Optimized for reduced mobility cost without masks!
Added shaping for wide spectrum of assistance profiles
[4] Sawicki et al. (2009), Exercise and Sport Sciences Reviews 37(3)

## Slide 8: Personalized, human-in-the-loop optimization
Label | RMSE, Stroke | R2, Stroke
Hip Power | 0.18 | 0.58
Hip Angular Velocity | 0.37 | 0.88
Knee Power | 0.20 | 0.54
Ankle Power | 0.23 | 0.76
Hip Torque (current) | 0.18 | 0.65
Mjoint*
Texo
Pexo(+)
+
-
Ang veljoint*
Pbio(+)
Introduction
Generalizable controller
Optimization
Conclusion

## Slide 9: Personalized, human-in-the-loop optimization
Mjoint*
Pjoint*(+)
Texo
Pexo(+)
+
-
Ang veljoint*
Pbio(+)
Our proposed 3 parameters, scale, delay, and now shape, opening up beyond biotorque
Introduction
Generalizable controller
Optimization
Conclusion

## Slide 10: Preliminary experimental results
OFFLINE: We are assuming knee and ankle power are unaltered. Same kinematics regardless of profile – just walking
High scales and low shapes are preferred
120-180ms as expected, [2]
[2] Molinaro et al. (2024), Science Robotics 9

## Slide 11: Preliminary experimental results
-14.2%
First AB pilot test. 14.2% reduction in estimated power vs vanilla (30% scale, no delay, λ=1)
N = 1, AB
Best parameters: scale ≈ 20%, add. delay ≈ 25ms, λ ≈ 1.2
Unequal results between legs in AB, potentially lack of convergence and stroke-only TCNs
Introduction
Generalizable controller
Optimization
Conclusion
*Each iteration is 1 minute long

## Slide 12: Conclusion
Developed a user-state-trained controller and Bayesian optimizer for hip exoskeleton assistance for stroke with N=20 TCNs
Developed a task-agnostic, biotorque shaping paradigm for reduced energy cost without metabolic masks required
Conducted successful offline and pilot experiments to identify optimal torque parameters
Ready to launch final experiments in stroke populations, targeting personalized assistance profiles and evaluating metabolic and muscle activation improvements
Introduction
Generalizable controller
Optimization
Conclusion

## Slide 13: PERSONALIZED EXOSKELETON CONTROL FOR OPTIMIZING GAIT ECONOMY IN STROKE SURVIVORS
Daniel Rodriguez-Jorge, Gregory Sawicki, Aaron Young
August 14th, 2025
American Society of Biomechanics (Pittsburgh, PA)
Advances in Biomechanics with the power of AI & ML